## Slide 1: EC/b+ Experiment with CaMoO4 crystal.
WoonGu Kang, Yeongduk Kim
Sejong University
4th Amore Meeting
2011. 9. 28

## Slide 2: Motivation of EC/EC
Though the detection of 0nbb decay would prove the existence of massive Majorana neutrinos, the possible mechanisms giving rise to 0nbb decay would be uncertain.
  exchange of light Majorana neutrinos.
  Heavy neutrino exchange
  right-handed currents
  R-parity violating supersymmetry.
It would be possible to disentangle the possible mechanisms by comparing the half-lives of 0nbb and 0nb+/EC DBD.

## Slide 3: Some best 2, +, 2+ experiments
Nuclide | Channel | Experimental limits T1/2 (yr) | Technique
40Ca | 2 | > (3-6) ×1021 | CaF2(Eu) scintillators
54Fe | 2 | > (4-5) ×1020 | HPGe  spectrometry
58Ni | 2, + | > (0.2-7)×1020 | HPGe  spectrometry
64Zn | 2, + | > (0.06-7)×1020 | ZnWO4 scintillators
78Kr | 2, +, 2+ | > (1-5)×1021 | Gaseous detector
92Mo | 2, + | > (0.06-9)×1020 | HPGe  spectrometry
96Ru | 2, +, 2+ | > (0.2-1.3)×1019 | HPGe  spectrometry
106Cd | 2, +, 2+ | > (0.01-4)×1020 | HPGe  spectrometry, NaI(Tl)  spectrometry CdWO4 scintillators CdZnTe semiconductor
130Ba | 2, +, 2+ | > 4×1021 = (2.2 ± 0.5) ×1021 | Geochemical Geochemical
132Ba | 2 | > 2.2×1021 | Geochemical
F.A. Danevich Workshop on Double Beta Decay Search, SNU 15 Oct 2009
Even 2nECEC Not detected for any nucleus !

## Slide 4: 106Cd EC/EC

## Slide 5: TGV II
Location: Modane Underground
Laboratory (4800 m.w.e.)
Copper
> 20 cm
Airtight box
Lead >10cm
Boron filled polyethylene 16cm
HPGe
HPGe
Cd
Notes: flux [1/s]
fluence [1/m2]
fluence rate = flux density [1/s.m2]
na povrchu je neutron flux cca 40 / m2.s

## Slide 8: β+EC decay of 92Mo
511keV γ
511keV γ
Gamma detector
Active crystal
with 92Mo
Conceptual setup
EC/β+ Q-value=628keV, ECEC = 1,650keV
Abundance = 92Mo: 14.84%, 100Mo: 9.63%
e+ stops in active(CaMoO4) Crystal.
92Mo nucleus is EC/EC or EC/b+ isotope.
(A,Z) + e- -> (A,Z-2 ) + e+ + 628keV
Notes: Mo-92 nucleus is double EC and beta plus EC isotope.
And This is double beta decay scheme from mo-92 to Zr-92.
Q-value of the double EC is 1650keV and EC beta plus is 628keV.
If camoo4 crystal is used for mo-92 decay, we can use the triple coincidence with the 628keV of the camoo4 and 511keV in 2 CsI crystals.
So you can see here the conceptual setup.
If the positron stops inside camoo4 crystal, then two 511keV gammas emit b2b direction.
The abundance of Mo-92 is 14.84%.

## Slide 9: Experimental setup at Y2L
CsI10
CsI9
CsI8
CsI7
CaMoO4
CsI11
CsI12
CsI1
CsI2
CsI3
CsI4
CsI5
CsI6
e+
511keV
511keV
628keV(Q-value)
CsI detectors surround the CaMoO4 crystal
511keV signal is a opposite direction for momentum conservation.
(back to back cut)
CaMoO4 is surrounded by 14 CsI crystals & 14 PMTs.
pmt
CsI CaMoO4
  6.5x5.5x30cm(12) - 2.2x2.2x6cm (2)
  9x9x6cm(#13 & #14) - 255g
PMTs & CsI crystals are crossly connected.
Lead shielding(10 cm)
Notes: This is a picture of detector setup at the y2l underground lab in korea.
Here photos are before and after attachment of the pmt. And lead shielding is 10cm.
Camoo4 is located in the center of the cavity and 14 csi detector array. And 511keV gammas are in opposite direction.
We are using b2b coincidence condition.
There are 12 csi crystals with a size….
And 2 of this crystals are coupled together and attached to pmt.
The total mass of camoo4 crystal is 255g.

## Slide 10: Background spectrum of CaMoO4 detector measured at Y2L
We used 1inch pmt in the middle of the experiment
for the other SrCl2 crystal test.
40K contamination increased.

## Slide 11: Background simulation
U - CsI(Tl) crystals
Th - CsI(Tl) crystals
K – 1inch PMT
K – CsI(Tl) crystals
K – CaMoO4 crystal
CaMoO4
CsI(Tl)
PMT
External
(rock)
Uranium
Thorium
Potassium

## Slide 12: Background simulation & gaussian fit result
= 2.3 x 1020y
Log2=0.693,
m = 276.8g,
α = 0.1484,
A0 = 6.02x1023
η = 0.122,
T = 341day = 0.93year
A = 204g,
N90 = 2.1 ± 25 counts
Notes: In the camoo4 and CsI spectrum with 2 511keV +-2sigma b2b coincidence gammas, we see 2.1events in the window of 628keV energy region by red fitted result. Then this number gives 2.3 x 10^20 years with 90%C.L. this limit is a comparable best.

## Slide 13: Optimizing CaMoO4+HPGe
■ Double beta decay experiment using HPGe detector
■ Geant4 simulation  find optimize size
135.5
94.12
84.84
78.36
100.0 +thickness
thickness
thickness
100.0+thickness
thickness [mm]
10
20
30
40
50

## Slide 14: Simulation for Mo92 EC b+ Decay
627keV<628keV<629keV : camoo4
510keV<511keV<512keV : ge
±1keV region
Notes: The left figure is efficiency curve for a correction between ge and camoo4 deposit energy
In figure, the x-axis is crystal thickness. And in this case of increase thickness,
the efficiency curve is decrease because decrease deposit energy probability for 628kev and 511kev

## Slide 15: EC/ b+ w/ HPGe
105mm
e+ signal
511keV
HPGe
Detector
PMT R0= 76mm
Photocathode R1= 64mm
R1
R0
50mm
25mm
Crystal mass230g
1460keV gamma from 40K Compton scatters.
Background or 0v EC/b+
R1

## Slide 16: New HPGe detector Setup
Mass | Diameter | Height
2.8kg | 82.1 mm | 90.7 mm
100% relative efficiency

## Slide 17: B.G comparison of ORTEC and CANBERRA
CANBERRA is lower than ORTEC.
Ra226
Bi214
K40
Tl208
Th232
U238
□ : ORTEC ● : CANBERRA

## Slide 18: DAQ setup
HPGe
Detector
FADC400
Pre-Amp
x10
Data
Acquisition
Shaping
Amp
511keV
e+ signal
CaMoO4 crystal
Pre-Amp signal과 Shaping Amp signal
FADC
Pre-Amp
Ch1
Ch2(1/3)
Ch3

## Slide 19: Hamamatsu 3” Metal PMT
■ The R11065 is 3” Metal PMT
extremely low radioactivity
■ High QE : 22% @ 450nm

## Slide 20: Typical Signals from FADC
CaMoO4 Signal
0~700keV
HPGe Signal
0keV~700eV
HPGe Preamp Signal
0keV~3000keV
HPGe signal
700keV~3000keV

## Slide 21: Energy Calibration
Ba133 Source
Cs137 Source
Co60 Source
HPGe Detector
Cs137 Source
661.657 keV
FWHM : 18%
CaMoO4 Crystal

## Slide 22: Rates
* After 2days, gets stabilized.
days

## Slide 23
One event within 2 days, and no event until 11 days.
After energy calibration.
CaMoO4 628.0 ±62.8 [keV]
HPGe 511.0 ±2keV [keV]
1 event /9 days in the gate

## Slide 24
HPGe energy spectra
Black : total spectrum (0~11days)
rate = 0.19 Hz
Red : spectrum after 2days
rate = 0.16 Hz
Blue : w/ camoo4 crystal coincidence.
rate = 0.10 Hz

## Slide 25
CaMoO4
Ge
One strange coincidences : CaMoO4(1240keV) &
HPGe( 60keV )

## Slide 26: Conclusion & summary
Initial EC/b+ 0nbb limit is 2.3 x 1020y with 92Mo.
CaMoO4+HPGe data taken with a CaMoO4 crystal.
Scale-up should be studied by simulation.
Low-temperature option can be considered.

## Slide 27: Resolution of CaMoO4 crystal

## Slide 28
1240keV와60keV의 coincidence이벤트 count rate 변화
Blue->Ge, Red = CaMoO4